DESIGN

I. Problem statement :

To design and implement a array sorting system using a TCP based client-server program in C.

II. Socket functions used :

 On the client side, the following functions from the standard C libraries, <fcntl.h> ,<sys/types.h> and <sys/socket.h> are included:

1. socket():
Use: To get the file descriptor
Syntax: int socket(int domain, int type, int protocol);
2. connect():
Used to connect using PF_INET and SOCK_STREAM.
3. send() and recv() are used to send messages to and from the server.
4. close():
Used to close the socket connection.

On the server side, the following functions from the standard C libraries,<fcntl.h>, <sys/types.h> and <sys/socket.h> are included:

1. socket():
Use: To get the file descriptor
Syntax: int socket(int domain, int type, int protocol);
2. connect():
Used to connect using PF_INET and SOCK_STREAM.
3. bind():
Used to bind the port number with the corresponding socket.
4. accept():
Used to acccept the incoming connection.
5. listen():
Listens to incoming requests from clients.
6. send() and recv() are used to send messages to and from the server.
7. close():
Used to close the socket connection

III. Design :

1. Sockets are created on both the socket side and the client side.
2. The server is the listen() mode.
3. The client first connects to the server using connect().
4. bind() system call is used in the server side to bind the port number to the socket.
5. The server accepts the incoming connection from a client using accept().
6. The client first asks for size of array.
7. Subsequently, the client gets input array and sends to server using send()
9. Server receives using recv()
8. Server reverse the array and send back